## Slide 1
IOT

## Slide 2
Group members
Thùy Dương
SE171916
Group 3
Đức Đạt
SE171888
Văn Quyến
SE171910
Đoan Trinh
SE171941
Minh Thư
SE171876

## Slide 3
1
2
3
0
WELCOME
NodeMCU ESP8266.
Notes: NodeMCU ESP8266

## Slide 4
1
2
3
4
5
0
WELCOME
NodeMCU ESP8266.
BLUETOOH MODULE
Notes: BLUETOOTH MODULE

## Slide 5
1
2
3
4
5
0
WELCOME
BLUETOOH MODULE
MODULE MATRIX 8x32 LED
Notes: Module Matrix 8x32 LED

## Slide 6
WELCOME
NodeMCU ESP8266
configuration
function
use
services
operation
Notes: Configuration

## Slide 7
configuration
function
use
services
CONFIGURATION
- Microcontroller: The CPU is a 32-bit Tensilica Xtensa LX106 RISC processor
- Operating voltage: 3.3V
- Input voltage: 7-12V from the VIN pin or 5V from the micro USB port.
- Digital I/O pins (DIO): 16
- Analog input pins (ADC): 1
- Interfaces: UART, SPI, I2C
- Flash memory: 4 MB
- SRAM: 64 KB
- Clock speed: 80 MHz
- Types of pins include: Power, GND, GPIO, SPI, I2C, PWM, ADC, UART, SDIO, Control, Reserved.
operation
Notes: Operating voltage: 3.3V Types of pins include: Power, GND, GPIO, SPI, I2C, PWM, ADC, UART, SDIO, Control, Reserved.

## Slide 8
function
use
services
configuration
FUNCTION OF THE PINS
1. POWER PIN
2. GPIO pins (General-Purpose Input/Output pins)
- Total: 17 GPIO pins.
- Each GPIO can be configured internally to the either HIGH or LOW
operation
Notes: Each GPIO can be configured internally to be either HIGH or LOW.

## Slide 9
function
use
services
configuration
Which GPIO pins of ESP8266 are safe to use?
FUNCTION OF THE PINS
operation
Notes: Which GPIO pins of ESP8266 are safe to use?

## Slide 10
function
use
services
configuration
FUNCTION OF THE PINS
3. ADC PIN
- Read values: 0V  3.3V
- Analog value read from the ADC pin will be converted to a value ranging from 0 to 1023
4. SPI PIN
- Two main SPI types: Primary SPI (SPI) and Secondary SPI (HSPI).
- 80Hz
- Both support FIFO with a 64-byte buffer
operation
Notes: Both support FIFO (First-In-First-Out) with a 64-byte buffer.

## Slide 11
function
operation
use
services
configuration
FUNCTION OF THE PINS
5. I2C PIN
- GPIO4 (SDA) và GPIO5 (SCL)
- wire.begin(SDA, SCL)
6. UART PIN
- UART0 và UART1
- TXD0 (Transmit Data 0), RXD0 (Receive Data 0), RST0 (Reset 0) và CTS0 (Clear To Send 0)
- UART1 communication  TXD1 (Transmit Data 1) pin.
Notes: Both support FIFO (First-In-First-Out) with a 64-byte buffer.

## Slide 12
function
use
services
configuration
FUNCTION OF THE PINS
7. PWM PIN
- From GPIO0 to GPIO15
- ESP8266: PWM signals 10-bit resolution
8. SDIO PIN
- Supports SDIO v1.1 (4-bit 25 MHz) and SDIO v2.0 (4-bit 50 MHz).
- Frequency range of PWM signal: ~100Hz to 1kHz. Time period: ~1000 μs to 10000 μs.
operation
Notes: frequency range of the PWM signal is from approximately 100 Hz to 1 kHz.

## Slide 13
function
use
services
configuration
FUNCTION OF THE PINS
9. INTERRUPT PIN
All GPIO pins, except GPIO16.
operation
Notes: Interrupt

## Slide 14
function
use
services
configuration
FUNCTION OF THE PINS
- EN Pin (CH_PD hoặc Chip Power Down):
10. CONTROL PIN
+ Default: HIGH level
+ When pulled up to a HIGH level: chip is activated. LOW: chip is disabled
- RST pin:
+ Default: HIGH level
+ When brought down to a LOW level for a short period: restart.
- FLASH pin:
+ Determines when to enter programming mode during startup.
+ LOW level during startup: initiates the programming process.
- WAKE pin:
+ Wake up the ESP8266 from deep sleep mode.
operation
Notes: Interrupt

## Slide 15
function
configuration
operation
use
services
PRINCIPLE OF OPERATION
1. Boot
2. System and Memory Initialization
3. Environment Check.
4. Wi-Fi Initialization
5. Run User Program
6. GPIO Communication and Sensor Interaction
7. Wi-Fi Communication and MQTT/HTTP
8. Power Saving Mode
9. UART (Serial Communication)

## Slide 16
function
timeline
use
services
configuration
HOW TO USE
Connecting NodeMCU to the Computer:
Use a Micro USB cable to connect NodeMCU to your computer. Ensure that NodeMCU is recognized and has the appropriate drivers installed

## Slide 17
function
timeline
use
services
configuration
HOW TO USE
Write and Upload a Simple Program:
For example, you can use the Blink program to make the LED on NodeMCU flash.
● Check the Results
● Develop IoT Applications
● Wi-Fi Communication and MQTT
● Monitoring and Debugging

## Slide 18
function
timeline
use
services
Home automation.
Collecting data from sensors.
Measuring power consumption.
Internet Smoked Alarm
Controlling via Wi-Fi.
configuration
APPLICATION

## Slide 19
A
CONFIGURATION
1. Frequency: 2.4 GHz ISM band
2. Operating voltage: 3.3V to 5V
3. IC: BC417
4. Flash memory: 8Mbit
5. Bluetooth version: 2.0 + EDR (Enhanced Data Rate)
6. Bluetooth system: Bluetooth CSR Bluecore 04 external single chip with CMOS technology
B
55%
35%
35%
WRITE SOME TEXT HERE
C
A
B
C
D
65%
TYPE YOUR TEXT
65%
TYPE YOUR TEXT
55%
TYPE YOUR TEXT
85%
TYPE YOUR TEXT
25%
TYPE YOUR TEXT
35%
TYPE YOUR TEXT
CONFIGURATION
BLUETOOTH MODULE
FUNCTION OF THE PINS
PRINCIPLE OF OPERATION
HOW TO USE
APPLICATION

## Slide 20
A
7. Protocol: IEEE 802.15.1 standard
CONFIGURATION
1. Frequency: 2.4 GHz ISM band
2. Operating voltage: 3.3V to 5V
3. IC: BC417
4. Flash memory: 8Mbit
5. Bluetooth version: 2.0 + EDR (Enhanced Data Rate)
6. Bluetooth system: Bluetooth CSR Bluecore 04 external single chip with CMOS technology
B
55%
35%
35%
WRITE SOME TEXT HERE
C
A
B
C
D
65%
TYPE YOUR TEXT
65%
TYPE YOUR TEXT
55%
TYPE YOUR TEXT
85%
TYPE YOUR TEXT
25%
TYPE YOUR TEXT
35%
TYPE YOUR TEXT

## Slide 21
A
CONFIGURATION
1. Frequency: 2.4 GHz ISM band
2. Operating voltage: 3.3V to 5V
3. IC: BC417
4. Flash memory: 8Mbit
5. Bluetooth version: 2.0 + EDR (Enhanced Data Rate)
6. Bluetooth system: Bluetooth CSR Bluecore 04 external single chip with CMOS technology
7. Protocol: IEEE 802.15.1 standard
B
FUNCTION OF THE PINS
1. VCC: Connect 5 V or 3.3 V to this Pin
2. GND: Ground Pin of module
3. TXD: Transmit Serial data
4. RXD: Receive data serially
5. State: It tells whether module is connected or not.
6. Enable/Key: The pin changes mode between data mode and command line mode by providing an external signal
7. Button: Change data and command modes
8. LED: shows the status of Module HC-05
C
A
B
C
D
65%
TYPE YOUR TEXT
65%
TYPE YOUR TEXT
55%
TYPE YOUR TEXT
85%
TYPE YOUR TEXT
25%
TYPE YOUR TEXT
35%
TYPE YOUR TEXT

## Slide 22
A
CONFIGURATION
1. Frequency: 2.4 GHz ISM band
2. Operating voltage: 3.3V to 5V
3. IC: BC417
4. Flash memory: 8Mbit
5. Bluetooth version: 2.0 + EDR (Enhanced Data Rate)
6. Bluetooth system: Bluetooth CSR Bluecore 04 external single chip with CMOS technology
7. Protocol: IEEE 802.15.1 standard
B
C
A
B
C
D
65%
TYPE YOUR TEXT
65%
TYPE YOUR TEXT
55%
TYPE YOUR TEXT
85%
TYPE YOUR TEXT
25%
TYPE YOUR TEXT
35%
TYPE YOUR TEXT
PRINCIPLE OF OPERATION
- Based on sequential communication protocol.
- Receive data and remove the beginning and end, then pass it through UART.
- Builds a Bluetooth packet and sends it over a Bluetooth wireless connection to the receiving device
- HC-05 has two operating modes:
+ Command Mode:You can communicate with the Bluetooth module via AT commands
Ex: AT + NAME = ****** : To set/change device name
+ Data Mode: used to communicate with other Bluetooth devices

## Slide 23
A
CONFIGURATION
1. Frequency: 2.4 GHz ISM band
2. Operating voltage: 3.3V to 5V
3. IC: BC417
4. Flash memory: 8Mbit
5. Bluetooth version: 2.0 + EDR (Enhanced Data Rate)
6. Bluetooth system: Bluetooth CSR Bluecore 04 external single chip with CMOS technology
7. Protocol: IEEE 802.15.1 standard
B
PRINCIPLE OF OPERATIO
- Based on sequential communication protocol.
- Receive data and remove the beginning and end, then pass it through UART.
- Builds a Bluetooth packet and sends it over a Bluetooth wireless connection to the receiving device
- HC-05 has two operating modes:
+ Command Mode:You can communicate with the Bluetooth module via AT commands
Ex: AT + NAME = ****** : To set/change device name
+ Data Mode: used to communicate with other Bluetooth devices
C
HOW TO USE
1. The TX will communicate with the controller's RX and the RX will communicate with the microcontroller's TX
2. There is a third pin (Key) used to switch modes.
3. When no input signal is fed to the Key pin, the device will operate in data mode.
4. After feeding a logical input signal to this pin, the device enters command line mode.
D
65%
TYPE YOUR TEXT
65%
TYPE YOUR TEXT
55%
TYPE YOUR TEXT
85%
TYPE YOUR TEXT
25%
TYPE YOUR TEXT
35%
TYPE YOUR TEXT

## Slide 24
A
CONFIGURATION
1. Frequency: 2.4 GHz ISM band
2. Operating voltage: 3.3V to 5V
3. IC: BC417
4. Flash memory: 8Mbit
5. Bluetooth version: 2.0 + EDR (Enhanced Data Rate)
6. Bluetooth system: Bluetooth CSR Bluecore 04 external single chip with CMOS technology
7. Protocol: IEEE 802.15.1 standard
B
PRINCIPLE OF OPERATIO
- Based on sequential communication protocol.
- Receive data and remove the beginning and end, then pass it through UART.
- Builds a Bluetooth packet and sends it over a Bluetooth wireless connection to the receiving device
- HC-05 has two operating modes:
+ Command Mode:You can communicate with the Bluetooth module via AT commands
Ex: AT + NAME = ****** : To set/change device name
+ Data Mode: used to communicate with other Bluetooth devices
C
D
65%
TYPE YOUR TEXT
65%
TYPE YOUR TEXT
55%
TYPE YOUR TEXT
85%
TYPE YOUR TEXT
25%
TYPE YOUR TEXT
35%
TYPE YOUR TEXT
5. After entering command line mode, the module's default settings may change when using the following commands:
>> AT - To check the connection
>> AT + NAME = ****** - To set/change the device name
>> AT + UART = *****, *, * - To set the transfer rate, stop bit and parity bit
>>AT + VERSION? - Display version of Bluetooth module
>>AT + ORGL - The command to save settings has been executed
HOW TO USE

## Slide 25
A
CONFIGURATION
1. Frequency: 2.4 GHz ISM band
2. Operating voltage: 3.3V to 5V
3. IC: BC417
4. Flash memory: 8Mbit
5. Bluetooth version: 2.0 + EDR (Enhanced Data Rate)
6. Bluetooth system: Bluetooth CSR Bluecore 04 external single chip with CMOS technology
7. Protocol: IEEE 802.15.1 standard
B
PRINCIPLE OF OPERATIO
- Based on sequential communication protocol.
- Receive data and remove the beginning and end, then pass it through UART.
- Builds a Bluetooth packet and sends it over a Bluetooth wireless connection to the receiving device
- HC-05 has two operating modes:
+ Command Mode:You can communicate with the Bluetooth module via AT commands
Ex: AT + NAME = ****** : To set/change device name
+ Data Mode: used to communicate with other Bluetooth devices
C
D
65%
TYPE YOUR TEXT
65%
TYPE YOUR TEXT
55%
TYPE YOUR TEXT
85%
TYPE YOUR TEXT
25%
TYPE YOUR TEXT
35%
TYPE YOUR TEXT
6. When the KEY pin is not plugged into the computer, it is connected to GND (Data mode)
7. After plugging into the computer, we change the KEY pin through the 3V3 port (Command mode)
8. Open the serial and switch Baud to 38400 then switch back to 9600 (baud rate adjustment)
HOW TO USE

## Slide 26
A
CONFIGURATION
1. Frequency: 2.4 GHz ISM band
2. Operating voltage: 3.3V to 5V
3. IC: BC417
4. Flash memory: 8Mbit
5. Bluetooth version: 2.0 + EDR (Enhanced Data Rate)
6. Bluetooth system: Bluetooth CSR Bluecore 04 external single chip with CMOS technology
7. Protocol: IEEE 802.15.1 standard
B
PRINCIPLE OF OPERATIO
- Based on sequential communication protocol.
- Receive data and remove the beginning and end, then pass it through UART.
- Builds a Bluetooth packet and sends it over a Bluetooth wireless connection to the receiving device
- HC-05 has two operating modes:
+ Command Mode:You can communicate with the Bluetooth module via AT commands
Ex: AT + NAME = ****** : To set/change device name
+ Data Mode: used to communicate with other Bluetooth devices
C
HOW TO USE
6. When the KEY pin is not plugged into the computer, it is connected to GND (Data mode)
7. After plugging into the computer, we change the KEY pin via VCC 5V (or through the 3V3) (Command mode)
8. Open the serial and switch Baud to 38400 then switch back to 9600 (baud rate adjustment)
D
FUNCTION OF THE PINS
1. Embedded project.
2. Data transfer between two HC-05 modules.
3. Send data from HC-05 to another Bluetooth device.
4. Control the device remotely via Bluetooth.
5. Control the robot via Bluetooth.
6. Wireless headphones and mouse.

## Slide 27
Welcome to Module Matrix 8x32 LED
MAX7219 Arduino Xanh Dương MT-832-G
Slide 1
Slide 2
Slide 3
Slide 4
Slide 5
Slide 6

## Slide 28
Slide 1
CONFIGURATION
● Size: 8x32 LEDs, consisting of 4 matrices 8x8 stitched together.
Slide 2
Slide 3
Slide 4
Slide 5
Slide 6
● Blue LED Matrix
● Operating Voltage: 5V
● IC driver: MAX7219
● Dimensions: Length: 130mm. Height: 32mm. Width: 14mm
● Communication follows the SPI standard, utilizing RCLK and DIO.
Notes: Configuration

## Slide 29
Slide 1
Slide 2
PRINCIPLE OF OPERATION
Slide 3
Slide 4
Slide 5
Slide 6
8 Rows
32 Columns
8 Rows
8 Columns
Notes: Principle of operation

## Slide 30
Slide 1
Slide 2
PRINCIPLE OF OPERATION
Slide 3
Slide 4
Slide 5
Slide 6
Notes: Principle of operation

## Slide 31
Slide 1
Slide 2
PRINCIPLE OF OPERATION
Slide 3
Slide 4
Slide 5
Slide 6
Row
Column
Cathode
Anode
● Connecting all rows and columns together is done to reduce the number of pins required to control each LED dot.
 Multiplexing
Notes: Serial Peripheral Interface

## Slide 32
Slide 1
Slide 2
PRINCIPLE OF OPERATION
Slide 3
Slide 4
Slide 5
Slide 6
● MAX7219 is an Integrated Circuit (IC).
● Used to connect multiple LED displays or LED matrices.
● It reduces the complexity of controlling LEDs and displaying numbers or characters.
● It handles all control and refresh tasks  sent via SPI communication.
Notes: Principle of operationSerial Peripheral Interface

## Slide 33
Slide 1
Slide 2
PRINCIPLE OF OPERATION
Slide 3
Slide 4
Slide 5
Slide 6
Notes: Principle of operation

## Slide 34
Slide 1
Slide 2
PRINCIPLE OF OPERATION
Slide 3
Slide 4
Slide 5
Slide 6
● RSet resistor: used to adjust the brightness of the LED matrix.
● Control the maximum current supplied to the LED.
Notes: Principle of operation

## Slide 35
Slide 1
Slide 2
PRINCIPLE OF OPERATION
Slide 3
Slide 4
Slide 5
Slide 6
● Used to transmit and receive data from Arduino or any other data source.
● This communication includes: CLK (Clock), DIN (Data In), CS (Chip Select), and DOUT
SPI communication.
Notes: Principle of operation

## Slide 36
Slide 1
Slide 2
Slide 3
Slide 4
Slide 5
Slide 6
FUNCTION OF THE PINS
● VCC: Connected to 5V (Anode)
Input Connections
● GND: Ground connection (Cathode)
● DIN: Data In pin. Connect it to any digital pin of the microcontroller.
● CS: Chip Select (sometimes labeled as LOAD).
● CLK: Clock pin. This pin receives clock signals to synchronize the data transfer into IC.
Notes: Function of the pins

## Slide 37
Slide 1
Slide 2
Slide 3
Slide 4
Slide 5
Slide 6
FUNCTION OF THE PINS
● VCC: Connect to the 5V pin of the next module.
Output Connections
● GND: Connect to the GND pin of the next module.
● DOUT: Data Out pin, connects to the DIN pin of the next module.
● CS: Connect to the CS/LOAD of the next module.
● CLK: Connect to the CLK pin of the next module.
Notes: Function of the pins

## Slide 38
Slide 1
Slide 2
Slide 3
Slide 4
Slide 5
Slide 6
HOW TO USE
● VCC - 5V (VCC is the power supply pin)
● GND - GND
● DIN (Data In) - Digital 11 (This is the pin for transmitting data from the microcontroller to the MAX7219)
● CS - Digital 10 (pin for selecting the operation of the module)
● CLK (Clock pin) - Digital 13 (pin providing clock pulses for the MAX7219)

## Slide 39
Slide 1
Slide 2
Slide 3
Slide 4
Slide 5
Slide 6
HOW TO USE
● Provide functions to configure and control LED devices through SPI communication.
Include the two libraries: MD_MAX72xx and MD_Parola.
● An extension of MD_MAX72xx
● To simplify the display of text and create motion effects on the LED matrix

## Slide 40
Slide 1
Slide 2
Slide 3
Slide 4
Slide 5
Slide 6
HOW TO USE
● Combine the power of MD_MAX72xx for hardware control.
The reason for using both libraries:
● Leverage the flexibility of MD_Parola for displaying text and effects.
Open Arduino IDE → select Sketch → Include Library → Manage Libraries, then search for "MD_MAX72xx".
To install:

## Slide 41
Slide 1
Slide 2
Slide 3
Slide 4
Slide 5
Slide 6

## Slide 42
Slide 1
Slide 2
Slide 3
Slide 4
Slide 5
Slide 6
APPLICATION
Display Weather Information
Clock and Alarm
Display Messages and Notifications
Display Traffic Route Information
Scrolling Text and Text Effects
Notes: Application

## Slide 43
Thank you for watching